Introduction to
Software Defined Radio

---
Agenda
- Materials
- What is SDR?
- The Basics
- SDR & Security
- Demonstrations
- Q & A
- thejoeblankenship.com
- joe@cgrii.org
- @CGRIIorg on Twitter

---
Materials
- Laptop (Ubuntu or other Linux OS)
  - GNU radio (can download Ubuntu image with GNU radio from GNURadio website)
- RTL-SDR dongle (NooElec R820T DVB-T is what I used)
- Antenna and cables

---
What is Software Defined Radio?
Software Defined Radio (SDR) in general
Basic reception, modulation/demodulation, and filtering defined in software
Digital Signal Processing (DSP) algorithms implemented in configurable hardware and/or PC software
SDR is NOT:
A computer-controlled conventional radio
A conventional radio with a GUI integrated into its front panel

---
The Basics
- Hardware
  - Receivers vs. Transceivers
  - Frequency/Signal Dependent
    - Antennas
    - Environment
  - Price/Functionality
  - Stay Flexible!
- Software
  - Up to you
Faraday Approved!

---
The NooElec RTL-SDR receiver uses the Rafael Micro RTL2832-R820T tuner chipset with MCX connector input
Widely supported by large hobbyist community
Has range of ~25MHz to ~1750MHz
There is no “one size fits all” antenna
The discone antenna is a good all-purpose antenna for VHF/UHF transmission, but has limits
For HAM Radio applications, the HamItUp can be used to interface with the NooElec receiver
Requires connector adapters
Provides additional gain while shifting all HF signals into the VHF range

---
Don't do this... unless you really want to

---
- Other options
  - USRP
    - More expensive
    - Much more functionality
  - Terratec t stick +
    - 53 – 2200 MHz
  - FunCube Dongle
    - Similar to NooElec
    - 64 - 1,700 MHz

---
- Other options
  - B200
    - Reasonable price
    - Good functionality
    - 70M to 6G
  - Hack RF
    - Half the price of B200
    - Half Duplex :(
    - 1M to 6G (reportedly 200k to 7.2G)

---
- Things you can do with SDR
  - Basic Radio broadcasts
    - Must comply with FCC
  - Amateur Radio
    - License to transmit
  - Radio Astronomy
  - Track AIS (Automatic Identification System)
  - Track Mode S (Aircraft)
  - Build a GSM network
    - FCC strikes again!!!
  - Construct your own secure communication network
    - Guerrilla radio at your own risk
  - Satellite packet collection and more!

---
- Several Online Resources
  - FCC
    - Publicly available resources
    - All laws regarding reception and transmission
  - Community Sites
    - RTL-SDR.com
    - RTLSDR.org
  - Other Hobbyist sites
    - http://superkuh.com/rtlsdr.html
  - Balint Seeber's page
    - http://spench.net/drupal/research/sdr
    - http://wiki.spench.net/wiki/Presentations
  - GNURadio Course Videos
    - https://www.youtube.com/playlist?list=PL618122BD66C8B3C4&feature=view_all
  - AMSAT
    - http://www.amsat.org/
  - Other
    - https://www.radioreference.com/apps/db/?ctid=1022

---
SDR for Security?
- Data transfer is increasingly wireless
  - Multi-modal vulnerabilities
    - (cellular, WiFi, Bluetooth, RFID… any EMR)
- Vulnerabilities are best found by you; not them
  - Many security devices not built securely
  - They often leak EM signals
  - Attack vectors will only increase, more rapidly, over time
- Helps security professionals think differently

---
- Final Notes
  - It does require some basic knowledge of radio theory
  - Programming/electronics knowledge is also a plus
  - Don't get frustrated... “Radio Happens”
  - If you can think it, you can probably do it... possibly

---
Demonstrations
- “Hello World” Dial tone (GNURadio)
- FM Radio (GNURadio)
- VHF/UHF Radio (gqrx)
- Mode S Collection (Dump1090)

---
Any Questions?